| FILM CAMERA PREP CHECKLIST |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | SPREADER |
|  | Runners slide smoothly and lock in all positions. |
|  | Tripod points fit into spreader receptacles. |
|  | TRIPODS – BABY & STANDARD |
|  | Legs slide smoothly and lock in all positions. |
|  | Top casting accommodates the head base (flat or bowl). |
|  | Wooden legs are free from cracks and splinters. |
|  | HIGH HAT OR LOW HAT |
|  | Mounted on smooth flat piece of wood or other suitable material. |
|  | Top casting accommodates the head base (flat or bowl). |
|  | FLUID HEAD |
|  | Base fits top casting of tripod and locks securely (Mitchell flat base or bowl shape). |
|  | Camera lock down screw fits into camera body, adapter plate or sliding base plate. |
|  | Pan and tilt movement is smooth at all tension settings. |
|  | Tension adjustments for pan or tilt engage and do not slip. |
|  | Pan and tilt locks securely at all settings. |
|  | Eyepiece leveler attaches to head securely. |
|  | Head contains a mounting bracket for the front box. |
|  | DUTCH HEAD |
|  | Easily mounted to main fluid head. |
|  | Tilt movement is smooth at all tension settings. |
|  | Tension adjustments for tilt engage securely and do not slip. |
|  | Tilt locks securely at all settings. |
|  | GEAR HEAD |
|  | Base fits tripod top casting and locks securely. (All gear heads should have a Mitchell flat base). |
|  | Camera lock down screw fits into camera body, adapter plate or sliding base plate. |
|  | Pan and tilt movement is smooth at all speed settings. Pan and tilt locks securely at all settings. |
|  | Gears shift smoothly. |
|  | Tilt plate operates smoothly and locks securely in all positions. (Only on gear heads with built in tilt plate.) |
|  | Eyepiece leveler attaches to head securely. |
|  | Head contains a mounting bracket for the front box. |
|  | SLIDING BASE PLATE |
|  | Mounts securely onto head and adapter plate mounts securely onto camera. |
|  | Slides smoothly and locks in all positions. |
| CPC | © DEE |

| FILM CAMERA PREP CHECKLIST – page 2 |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | CAMERA BODY |
|  | Fits securely on head or adapter plate. |
|  | Interior and exterior is clean and free of dirt and dust. Interior is free of emulsion buildup and film chips. |
|  | Aperture plate, pressure plate and gate areas are clean and free of any burrs. |
|  | Pressure plate is easily removable. |
|  | Lens port opening is clean. |
|  | Mirror is clean and free from scratches. (Do not clean mirror yourself) |
|  | Magazine port opening is clean. |
|  | On certain cameras, especially Panavision, electrical contacts in the magazine port opening are clean. |
|  | Footage counter and tachometer function properly. |
|  | On-off switch functions properly. |
|  | The movement of the shutter, pull-down claw, and registration pin is synchronized. |
|  | The mirror shutter stops in the viewing position when the camera is switched off. |
|  | Pitch control functions properly to quiet camera. |
|  | The variable speed switch functions properly. |
|  | Ground glass is clean and is marked for the correct aspect ratio. |
|  | Variable shutter operates smoothly through its entire range of openings. |
|  | Doors close tightly and latches lock securely to protect from light leaks. |
|  | Contrast viewing filter on eyepiece functions properly. |
|  | Behind-the-lens filter slot is clear and free of any obstruction. |
|  | Illuminated ground glass markings function properly and are adjustable in intensity. (If ground glass is removed, be sure to re-insert it properly.) |
|  | Rain covers are available and fit properly for all lens and magazine configurations. |
|  | VIEWFINDER |
|  | Long and short eyepieces mount properly and focus easily to the eye. |
|  | Eyepiece heater and magazine heater functions properly. |
|  | Eyepiece magnifier functions properly. |
|  | Diopter adjustment functions properly. |
|  | Contrast viewing filters work correctly. |
|  | FOCUS EYEPIECE |
|  | Set eyepiece diopter for your vision. |
|  | With lens removed, point camera at a bright light source. |
|  | While looking through eyepiece, turn the diopter adjustment ring until the crosshairs or grains of the ground glass are sharp. |
|  | If possible, lock the adjustment ring and mark it so that it can be returned to your setting if it should get moved. |
| CPC | © DEE |

| FILM CAMERA PREP CHECKLIST – page 3 |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | MAGAZINES |
|  | Fit securely on camera body. |
|  | Doors fit properly and lock securely |
|  | Interior is clean and free of dirt, dust and film chips. |
|  | Footage counter functions properly. |
|  | Have different size magazines for various shooting situations. |
|  | Magazine torque motor functions to properly to take-up film. |
|  | Magazine heater (if available) functions properly. |
|  | Electrical contacts on magazine are clean and function properly. |
|  | CAMERA AND MAGAZINE BARNEYS |
|  | Obtain proper size barneys for cameras and magazines. |
|  | Check heated barneys to be sure that they function properly. |
|  | SCRATCH TEST MAGAZINES |
|  | Check all magazines on all cameras. |
|  | Load a dummy load (approximately 20-30 feet) into each magazine. |
|  | Place magazine on camera and thread film in camera. |
|  | Run approximately 10-20 feet of film through the magazine. |
|  | Remove film from take-up side and examine under bright light for any scratches. Check emulsion side and base side for scratches. |
|  | When using high speed or variable speed cameras check magazines at various speeds. |
|  | LENSES |
|  | Contains the proper mount for the camera being used. |
|  | Lens seats properly in camera body. |
|  | Mirror shutter does not strike rear element of lens when spinning. |
|  | Front and rear glass elements are clean and free from scratches. |
|  | Front element coating is not scratched or worn away. |
|  | Iris (t-stop) diaphragm operates smoothly. |
|  | Focus gear threads properly. |
|  | Focus distance marks are accurate. |
|  | On zoom lenses the zoom motor operates smoothly. |
|  | Zoom lens tracks properly. (See below) |
|  | Lens shade mounts securely to each lens. |
|  | Zoom lens holds focus throughout the zoom range. |
|  | Matte box bellows fits securely around all lenses. |
|  | Obtain various size rubber donuts to insure a tight seal with matte box. |
|  | Support rods are proper size for the lens being used. |
| CPC | © DEE |

| FILM CAMERA PREP CHECKLIST – page 4 |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | ZOOM LENS – TRACKING |
|  | Place zoom lens on camera body. |
|  | Look through lens and line up the cross hair of the ground glass on a point in your prep area. |
|  | Lock the head so that the camera cannot pan or tilt. |
|  | Look through lens and slowly zoom lens all the way in to telephoto and all the way out to wide angle. |
|  | Look to see that the cross hair does not shift too noticeably from the original point. A small amount of shifting is acceptable. |
|  | If there is too much shifting (up/down or left/right) have the lens checked before taking it. |
|  | POWER ZOOM CONTROL & MOTOR |
|  | Check that zoom motor is mounted securely to lens. |
|  | Connect zoom control and motor and check that they function properly. |
|  | Check all power cables to be sure that they are in working order. |
|  | ALL LENSES – CHECK FOCUS |
|  | Mount lens to camera. |
|  | Set aperture (t-stop) to its widest setting. |
|  | Using your tape measure, place a focus chart at a specific distance as marked on lens. |
|  | Look through viewfinder and focus chart to your eye. |
|  | Check that measured distance matches the eye focused distance. |
|  | Check each lens at various distances including closest focusing point and infinity. |
|  | When checking a zoom lens, set it to its most telephoto focal length for checking focus. |
|  | MATTE BOX |
|  | Mounts properly and securely to iris rods, camera body or lens. |
|  | Operates smoothly with each lens. |
|  | Does not vignette with wide angle lenses. |
|  | Contains the proper adapter rings and rubber donut or bellows for each lens. |
|  | Filter trays are the correct size and slide in and out smoothly. |
|  | Rotating filter rings operate smoothly and lock securely in position. |
|  | Geared filter trays operate smoothly. |
|  | Swing away matte box operates smoothly. |
|  | Eyebrow or shade mounts securely and can be adjusted easily. |
|  | Hard mattes mount securely and are the correct size for each lens. |
| CPC | © DEE |

| FILM CAMERA PREP CHECKLIST – page 5 |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | FOLLOW FOCUS MECHANISM |
|  | Check that follow focus mounts securely to iris rods or camera body. |
|  | Engage follow focus gear to lens gear. |
|  | Check that it operates smoothly with each lens. |
|  | Have correct focusing gears for zooms and primes. |
|  | FOLLOW FOCUS ACCESSORIES |
|  | Check all accessories to be sure that they fit and operate smoothly – focus whip, speed crank, right hand extension, marking disks, etc. |
|  | FILTERS |
|  | All filters are correct size for matte box and lens shades being used. |
|  | All filters are clean and free from scratches. |
|  | Rotating polarizer operates smoothly. |
|  | Filter set contains an optical flat. |
|  | When using more than one camera, have enough filters for all cameras. |
|  | Check graduated filters for hard or soft edge. |
|  | OBIE LIGHT OR EYE LIGHT |
|  | Mounts securely to camera and operates correctly at each setting. |
|  | Spare bulb is included with light. |
|  | LENS LIGHT (ASSISTANT’S LIGHT) |
|  | Mounts securely to camera and is easily adjustable. |
|  | Spare bulb and power cable is provided. |
|  | PRECISION SPEED CONTROL |
|  | Mounts easily to camera and operates correctly for both high speed and slow motion. |
|  | Spare power cable is provided. |
|  | HMI SPEED CONTROL |
|  | Mounts easily to camera and operates correctly for both high speed and slow motion. |
|  | Spare power cable is provided. |
| CPC | © DEE |

| FILM CAMERA PREP CHECKLIST – page 6 |
| --- |
| Production Title |  |
| Camera Rental Company |  |
|  | SYNC BOX |
|  | Connect sync box and test to be sure that you can sync to computer screen or video monitor if necessary. |
|  | Camera must have an adjustable shutter in order to properly use the sync box. |
|  | VIDEO TAP & MONITOR |
|  | Connect video tap and monitor to be sure that you have proper image on screen. |
|  | Obtain extra cables and connectors. |
|  | Be sure that monitor can be powered from AC as well as battery power. |
|  | Check On-Board Video Monitor if one is being used. Be sure that it mounts securely to the camera. |
|  | HANDHELD ACCESSORIES |
|  | Obtain proper accessories and magazines if shooting any hand held shots – left and right hand grips, shoulder pad, light weight matte box, mini follow focus, on board or belt batteries, small magazines. |
|  | Mount all accessories and check for proper fit and comfort of operator. |
|  | Check hand grip with on/off switch to be sure that it functions properly. |
|  | REMOTE START SWITCH |
|  | Connect to camera and be sure that it functions properly. |
|  | Obtain extension cable for switch if necessary. |
|  | BATTERIES & CABLES |
|  | Have enough batteries for all cameras and accessories. |
|  | Check all cables for any frayed or loose wires. |
|  | Check that there are no loose pins in the plugs or connectors. |
|  | Check that all cables connect properly to camera body and batteries. |
|  | Obtain extra batteries if shooting in cold weather or when doing high speed work. |
|  | Obtain proper charges for all batteries being used. |
|  | Obtain extra power cables – each camera should have at least two power cables. |
|  | ADDITIONAL ITEMS |
| CPC | © DEE |